## Slide 1: Part 4
Mobile metric capture and reconstruction

## Slide 2: Acquisition vs Modeling
Modeling Subjective Reality
Acquisition Objective reality

## Slide 3: Acquisition – Measurable models

## Slide 4: Acquisition – Measurable models
75.3cm
75.3cm

## Slide 5: Acquisition – Measurable models
75.3cm
75.3cm

## Slide 6: Mobile metric acquisition
Commodity on-board instruments
  Camera
    Images
    Video
  Sensors
    Accelerometer
    Magnetometer
    Gyroscope
New generation devices
  i.e. SPC spherical panoramic camera
    One shot full-view panoramic images
    360 videos
    Integrated IMU
    Network

## Slide 7: Mobile metric reconstruction
Image-based
  Single image
    Vanishing points prior
    Geometric context prior
    Unified omnidirectional camera model
  Multi-view
    SfM pipelines
Mobile metric SfM pipeline
Tanskanen et al. ICCV2013
Garro et al. VMV2016

## Slide 8: Real-world applications: reconstruction of indoor scenes
Context
  Manual modeling
    Contractors create a floor plan respecting point-to-point laser measures
  High performance methods
    3D laser scanning/unstructured point clouds sources
      i.e. Mura et al.: Automatic room detection and reconstruction in cluttered indoor environments with complex room layouts. Computers & Graphics, 2014
  Computer vision/cost effective methods
    Interactive
      i.e. Kim et al.: Interactive acquisition of residential floor plans. In:Proc. IEEE ICRA, pp. 3055-3062 (2012)
    Semi-automatic: Images/SfM
      i.e. Furukawa et al.: Reconstructing building interiors from images. In: Proc. ICCV (2009)

## Slide 9: Reconstruction of indoor scenes
Manual modeling
  Contractors create a floor plan respecting point-to-point laser measures
High performance methods
  3D laser scanning/unstructured point clouds sources
    i.e. Mura et al.: Automatic room detection and reconstruction in cluttered indoor environments with complex room layouts. Computers & Graphics, 2014
Computer vision/cost effective methods
  Interactive
    i.e. Kim et al.: Interactive acquisition of residential floor plans. In:Proc. IEEE ICRA, pp. 3055-3062 (2012)
  Semi-automatic: Images/SfM
    i.e. Furukawa et al.: Reconstructing building interiors from images. In: Proc. ICCV (2009)
Require high-level skills
(computer experts, 3D modelers, or CAD operators)
Less performance
but less skills required

## Slide 10: Context: high performance methods
"Magic always comes with a price, Deary“ Rumplestiltskin
Once Upon a Time, ABC TV series
Limitation: lack in structure
  Details vs structure
  Need for complementary semi-automatic methods
Semi-automatic methods
  These usually have the goal of identifying walls, ceilings, and floors
  3D laser scanning/unstructured point clouds sources
      Mura et al.: Automatic room detection and reconstruction in cluttered indoor environments with complex room layouts. Computers & Graphics, 2014

## Slide 11: Context: interactive methods
New generation: Google Project TANGO
  Integrated depth sensor
  Mobile IMU (inertial measurement unit)
Background: depth sensors
  Es. Kinect based
    Kim et al.: Interactive acquisition of residential floor plans. In:Proc. IEEE ICRA, pp. 3055-3062 (2012)
Localization problems
  Short range
  Limited bounding volume
  Track ambiguities (pose registration)
  Map ambiguities (localization)

## Slide 12: Context: image-based methods
Automatic system for indoors/outdoors
  Goal: to reconstruct a simple 3D indoor model from multiple images
  Cost effective

## Slide 13: Multiview pipeline example
Images
SFM
MVS
MWS
Merging
Structure-from-Motion
Bundler by Noah Snavely
Structure from Motion for unordered image collections
http://phototour.cs.washington.edu/bundler/

## Slide 14: Multiview pipeline example
Images
SFM
MVS
MWS
Merging
PMVS by Yasutaka Furukawa and Jean Ponce
Patch-based Multi-View Stereo Software
http://grail.cs.washington.edu/software/pmvs/
Multi-view Stereo

## Slide 15: Multiview pipeline example
Images
SFM
MVS
MWS
Merging
Manhattan-World Stereo
[Furukawa et al., CVPR 2009]
Per-view depth maps using Markov random fields

## Slide 16: Multiview pipeline example
Images
SFM
MVS
MWS
Merging
Axis-aligned depth map merging
Volumetric MRF [Vogiatzis 2005, Sinha 2007, Zach 2007, Hernández 2007]

## Slide 17: Image-based methods: limitations
These methods produce high resolution 3D models and related aligned images but
  Lack of information about structure, real depth and scale
  Do not manage curved walls, sloped ceiling, etc.
  Do not return measurable models
Heavy use of Manhattan World assumptions
    MVS methods require textured surfaces, work poorly for many architectural scenes
    MW: scene structure is piecewise-axis-aligned-planar (i.e. corners must form right angles)
Next step
  Cabral R., Furukawa Y.: Piecewise planar and compact floor plan reconstruction from images. The IEEE Conference on Computer Vision and Pattern Recognition (2014)
  G. Pintore et al. Omnidirectional image capture on mobile devices for fast automatic generation of 2.5D indoor maps. In Proc. IEEE WACV2016
Notes: Examples of approaches are…

## Slide 18: Mobile devices to create floor plans
Many real-world applications focused on the structure of a building rather than the details of the model
  Definition of thermal zones
  Estimation for circulation of people in commercial/public/office buildings
  Support for evacuation simulation
  …
Growing interest
  Goal: Allow any user to reconstruct building interiors without the assistance of computer experts, 3D modelers, or CAD operators
  Next generation: Google Project Tango, PrimeSense Capri (Apple)
  SLAM-based methods [i.e. Shin et al.: Unsupervised construction of an indoor floor plan using a smartphone. IEEE Trans. Systems, Man, and Cybernetics (2012)]
Notes:   Such kind of multi-room mapping are useful in many real-world applications

## Slide 19: Mobile devices for multi-room mapping
MagicPlan - http://www.sensopia.com
  Floor corners marked via an augmented reality interface
  Manual editing of the room
  Floor plan merged manually
  Limits:
    Considerable errors: user must guess corner positions if occluded
    Time consuming (editing time)
Sankar and Seitz: Capturing indoor scenes with smartphones (UIST2012)
  Rooms geometrically calculated from the horizontal heading of the observer
  Corners marked during video playback
  Limits:
    Works only with Manhattan World scenes
    Rooms have arbitrary dimensions: need for manual scaling
    Manual identification of matching doors
Notes: In this context there is a growing interest in using mobile devices to create floor plans
Several works are already available:
MagicPlan reconstructs floor plans by marking floor corners visible from the room's center via an augmented reality interface. This approach manages also \emph{non-Manhattan world} scenes,
but requires manual editing for room assembly and is susceptible to error when floor corners are occluded by furniture, requiring
the user to guess their positions.

## Slide 20: Mobile devices for multi-room mapping
Sensors fusion approach
  Pintore et al.Interactive mapping of indoor building structures through mobile devices. In Proc. 3DV Workshop on 3D Computer Vision in the Built Environment, December Tokyo, 2014
  Pintore et al. Effective Mobile Mapping of Multi-room Indoor Structures. The Visual Computer, 30(6--8): 707-716, 2014
Compared to previous work
    Able to manage scenes not necessary limited to the Manhattan World assumption
    Produce 2D floor plans
      Automatically scaled to their metric dimensions
      Accurate enough to be used for simulations and interactive applications
20
Notes: We present a system to easily capture building interiors and automatically generate floor plans scaled to their metric dimensions. The proposed approach is able to manage scenes not necessarily limited to the \emph{Manhattan World} assumption, exploiting the redundancy of the instruments commonly available on commodity smartphones, such as accelerometer, magnetometer and camera. Without specialized training or equipment, our system can produce a 2D floor plan and a representative 3D model of the scene accurate enough to be used for simulations and interactive applications.

## Slide 21: Mobile devices for multi-room mapping
Scene capture
  Video of the room
    Ideal trajectory targeting the boundaries of the walls
  Every sample contains:
    3 angles q, g, r individuating boundary point at the current instant
    A time index t identifying the corresponding video frame
  Tracking of the passage to next room
  Matching doors/ graph update
Scene processing
  Combination of measures and images: room scaled to metric units
  Rooms placement step exploiting the scene graph information
Notes: Starting approximately from the center of the room, the user acquires a 360 degrees video of the environment, targeting with the phone camera the upper or lower boundaries of the walls, with a movement which traces an ideal trajectory along the intersection of the wall with the floor or with the ceiling.
When a room acquisition is completed the user moves to the next one aiming the phone camera to the exit door, whereas the application tracks his direction and updates a graph with the interconnections between the rooms.

## Slide 22: Mobile devices for multi-room mapping
Samples acquired imposing a linear trajectory
  Segment li (a,b): 2D line fitting the samples between qi-1 and qi
  But…
    Fitting directly the samples results in an inaccurate reconstruction
      Model approximation
      Instruments/human errors
    Occurrence of b in the den.: slope c2 / b = 0 non linear
  Weights wm calculated from the m video frames lying in the interval
Sd
qd

## Slide 23: Mobile devices for multi-room mapping
Simplified equation
  Can be minimized to determine a and b
For each line
  Fitting values: s2a,s2b,Q
  Scale and direction error
  Q depends from specific method
Placement of the rooms
  R0 best fitting values room
  Mi,i+1 2D transform from the matching door extremities
  Path to each room from the graph
  Absolute room positions
    MR3 = M2,3 * M1,2 * M0,1
    MR4 = M1,4 * M0,1
    …
R0
R1
R2
R3
M0,1
M1,2
M2,3
R4
M1,4
Origin

## Slide 24: Mobile devices for multi-room mapping
Enhancement
  Pintore et al.Interactive mapping of indoor building structures through mobile devices. In Proc. 3DV Workshop on 3D Computer Vision in the Built Environment, December Tokyo, 2014
  For each wall: coefficient of determination
    Weighted sum of residuals
    Weighted variance
  Each wall is marked as reliable or unreliable
  If the wall is unreliable we perform a further measurement step

## Slide 25: Mobile devices for multi-room mapping
For each room
  Set of corners: {c0…cn}
    {f0…fn} constant corner angles (calculated from walls orientation)
  All possible closed polygons P(d, ci)
    for:
      d varying between 0…360 degrees
      Ci possible starting point between {c0…cn}
    intersections {p0…pn} with the rays ray(origin, qi )
  Minimization of: d(dc, fc) = (1-l) dc + l fc
  d(dc, fc) includes:
    Angular error (absolute orientation, i.e. magnetometer)
    Distance error (manly user’s handle of device)
Ideal case: p5 coinciding with c5

## Slide 26: Mobile devices for multi-room mapping
Discussion
  Errors (10cm to 40 cm)
    Device sensors
    User handle
  The approximate structure can be exploited to bootstrap other methods (i.e. from unstructured point clouds sources, images, etc.)
  Future trend: integration of even more instruments on mobile devices (i.e. depth sensors)
    Full mobile pipeline to real-time capture, render and elaborate a 3D indoor environment

## Slide 27: Image-based A&R methods
Many advantages (see previous talks)
  Standard/perspective images
  Cost effective
  Implicit alignment between geometry and images
  …
Limitations
  Single-view: standard/perspective images lack information about the real depth
  Multi-view: require textured surfaces, and therefore work poorly for many architectural scenes
  Both approaches try to infer 3D clue imposing heavy constraints
    i.e. Manhattan World

## Slide 28: Image-based A&R methods
Single-view example
  A. Flint, C. Mei, D. Murray, and I. Reid. A dynamic programming approach to reconstructing building Interiors. In Proc. ECCV, pages 394–407. Springer, 2010
  A. Flint, D. Murray, and I. Reid. Manhattan scene understanding using monocular, stereo, and 3d features. In Proc. ICCV, pages 2228–2235, Nov 2011
  D. C. Lee, M. Hebert, and T. Kanade. Geometric reasoning for single image structure recovery. In Proc. CVPR, pages 2136–2143, 2009

## Slide 29: New approaches: omnidirectional images
Sources
  Specific sensors (fisheye camera, etc.)
  Images stitching (Microsoft ICE, Google PhotoSphere, etc.)
  Increasing diffusion
Advantages
  Wide field of view
  Minimize the possibility of fatal occlusions
  Help the tracking of features
  Contain more information than images from conventional cameras
  Potentially require less computation

## Slide 30: New approach: omnidirectional images
Common projections
  Fisheye
  Cylindrical
  ...
  Equirectangular
  Fisheye
  Cylindrical
  Equirectangular
  360 degrees
  180 degrees
Constraints
  All the corners must be visible
  Good stitching
  Vertical lines aligned with the gravity vector

## Slide 31: Reconstruction from equirectangular images
Planar and compact floorplan reconstruction from images
  R. Cabral and Y. Furukawa. Piecewise planar and compact floorplan reconstruction from images. In Proc. CVPR, June 2014.
  H. Yang and H. Zhang. Modeling room structure from indoor panorama. In Proc. VRCAI, 2014
Exploit previous work on perspective images
  Original unstitched images needed
  Virtual projections to recover views

## Slide 32: Reconstruction from equirectangular images
Planar and compact floorplan reconstruction from images

## Slide 33: Reconstruction from equirectangular images
Planar and compact floorplan reconstruction from images
Limitations
  3D data from MVS needed: original unstitched images required, inherits MVS problems (b and c)
  Geometry reasoning basically based on heavy piecewise planarity assumptions (d)
  Prior model needed

## Slide 34: Reconstruction from equirectangular images
Possible solutions
Ambiguity in vanishing points detection
What kind of model i need?
  How many corners?
  Unknown angles
Palazzo Sanjust - De Candia, V. Canelles, Cagliari
Chateau de Sermaise, France

## Slide 35: Reconstruction from equirectangular images
Projection in central catadioptric systems
  Bermudez-Cameo et al.: Hypercatadioptric line images for 3d orientation and image rectification. Robotics and Autonomous Systems, 2012

## Slide 36: Reconstruction from equirectangular images
Different view, different domain: Gh transform
  Geometric reasoning based on Pintore and E. Gobbetti. Effective mobile mapping of multi-room indoor structures. The Visual Computer, 30,2014. Proc. CGI 2014
  Gh maps all the points of the image in 3D space as if their height was h
q
g
0
360

## Slide 37: Reconstruction from equirectangular images
Gradient map
Model recovery
Transform
Accumulation points
q
g
0
360

## Slide 38: Reconstruction from equirectangular images
Shape and measures estimation
  Input: height of the point of view he (easy to estimate with a mobile device)
  Input: mobile image stitching (popular, i.e. Google PhotoSphere,etc.)
  Output: height of the walls hw
  Output: strong couples (M-samples)

## Slide 39: Reconstruction from equirectangular images
Shape and measures estimation
  Input: height of the point of view he
  Output: height of the walls hw

## Slide 40: Reconstruction from equirectangular images
Multi-room structure
  Minimal mobile tracking
  Doors matching
Room shape
  Global optimization
    2N parameters
    M-samples

## Slide 41: Examples

## Slide 42: Conclusions
New methods to automatically recover the shape of an indoor environment
    Not restricted to the Manhattan World assumption
    No need for externally calculated 3D data
    Designed to exploit the features of modern mobile devices
      Sensors fusion
      Capability to generate high-quality panorama images
    Can be easily extended to sloped ceiling
Future trend
  Hane et al. Real-time direct dense matching on fisheye images using plane-sweeping stereo. In Proc. 3DV, volume 1, pages 57–64, Dec 2014